## Slide 1: Line Following Robots

## Slide 2: Objectives
Move in straight lines
Basic Python will be learn through examples

## Slide 3: Robot
This mobile robots have only one sensor – infra red array.
black line absorb infra red while bright surface reflect infra red.
infra red travel in speed of light give almost zero delay between transmitter and receiver.

## Slide 4: What you going to do in this section
https://www.youtube.com/watch?v=e3iG1YwLLdQ&list=PLFrD3-dtN05EM5r5u3bSLUqNLjTn92jNp&index=2&t=0s

## Slide 5: Connect to WIFI
HAL 9000
password: imsorrydave

## Slide 6: Download required files from below link
pip install git+https://github.com/skyap/alphabot2.git

## Slide 7: Step by Step
All Programs -> Python -> IDLE
File -> New File

## Slide 8: Test Line Tracker
from alphabot2 import motor,line_tracker
import time
# IP adddress of your robot
address = "192.168.0.100"
# create line tracker object
lt = line_tracker.line_tracker(address)
# start reading data from server
lt.start()
for i in range(100):
# stop for one second
time.sleep(1)
if lt.data==0:
continue
# lt.data is an array with 5 elements
print(lt.data)
# remember to stop the socket connection
lt.stop()
To run the code:
F5
Run -> Run Module

## Slide 9: Test Motor (remember to put on floor before execution)
from alphabot2 import motor,line_tracker
import time
address = "192.168.0.100"
mot = motor.motor(address)
# below is the general function's parameters and range
# mot.command(direction,speed,duration)
# parameters:
# direction: "forward","backward","left","right","set_left_speed","set_right_speed","stop"
# speed: 0-100
# duration: second
# run forward at 20 speed for 5 seconds
mot.command("forward",20,5)
# set speed of left and right and ask robot to move forward
mot.command("set_left_speed",10)
mot.command("set_right_speed",10)
mot.command("forward")
time.sleep(5)
# stop moving , speed set to zero
mot.command("stop")
time.sleep(1)
# set speed of left and right and ask robot to move backward
mot.command("set_left_speed",10)
mot.command("set_right_speed",10)
mot.command("backward")
time.sleep(5)
mot.command("stop")
time.sleep(1)
# spin turn
mot.command("set_left_speed",10)
mot.command("set_right_speed",10)
mot.command("left")
time.sleep(5)
mot.command("stop")
time.sleep(1)
# spin turn
mot.command("set_left_speed",10)
mot.command("set_right_speed",10)
mot.command("right")
time.sleep(5)
mot.command("stop")
# remember to stop the socket connection
mot.stop()

## Slide 10: Now Let’s Talk about Rules
forward
left
right
u-turn
stop

## Slide 11: Let’s program it
use while loop
use if else condition

## Slide 12: Demostrations

## Slide 13: Any Questions?

## Slide 14: My Questions
Q1: Does the robot know whether it is moving after you give it a command?
Q2: How to let robot know it is moving after you command it?
Q3: How many combination of sensors available?